Scalable Configuration Interface
Scalable and easy to implement
  - Targeting dense register maps
  - Reduces area, wiring and congestion
- Half-duplex with request/ack pairs
  - Useful for low-speed register accesses
  - Latency insensitive!
- Inspired by SPI
  - Data bus is tri-stated
  - Has active-low chip select

---
SCI signals
N = number of peripherals
SIGNAL	WIDTH	DIRECTION	NOTES
CSN	N	Master->Slave	Master is busy and peripheral is considered selected as long as this signal stays low
REQ	1	Master->Slave	Requests are sent over this signal: operation type, address and data. Address and data are LSB first
RESP	1	Slave->Master	Data from the Slave during a Read are sent over this signal. Data is sent back LSB first
ACK	1	Slave->Master	Ack signal from the Slave to request the Master to reassert the chip select. It is also used as a strobe during Reads

---
Write example
- Example: Write 8’hf0 at address 4’ha
Address
Data
WNR
1’bZ undriven

---
Read example
- Example: Read from address 4’ha
Address
WNR
Data is not valid
Data is valid
Data

---
Architecture
Master
CSN/n+1
/1
/1
/1
Slave#n
Slave#1
Slave#0
REQ/1
RESP/1
3-state
buffers
ACK/1